High Performance Computing
Project Progress
Gaurav Kukreja
Evangelos Drossos

---
Planned Approach
- Scalasca Instrumentation – partially done
- Vectorization using Intrinsics – analyzing alternative approach using Intel Cilk
- Parallelization using OpenMP in SWE_Block - done
- Optimization of swe_mpi.c by overlapping communication and computation – in progress

---
Scalasca Instrumentation
- We have manually instrumented the SWE code
- To start with, we have made an analysis of the current implementation.
- As we optimize, we will compare our results and analyze the improvement.

---
Vectorization
- We are working on FwaveVec solver.
- We initially planned to use intrinsics to optimize vectorization.
- Instead, we will now use Intel Cilk for following reasons
  - Code is more readable, and easy to modify
  - Compiler should be able to exploit vectorization.

---
OpenMP
- Made appropriate changes to Sconstruct to make the existing OpenMP code compile.
- Minor optimizations like using schedule(static)
- Efficiency ~0.66 for 16 threads, with problem size 800 x 800
  - Reasons?
- Fused the loops inside computeNumericalFluxes, for a minor performance gain.
- Looking for further optimizations

---
OpenMP Results
* Problem Size 800x800

---
OpenMP Results
* Problem Size 1600x1600

---
MPI Optimization
- Studied the code in swe_mpi.c
- Identified points of improvement
  - Synchronous communication can be changed to asynchronous
    - Asynchronously send and receive Ghost Layers to/from appropriate threads
    - Perform computation of inner blocks
    - Ensure that Ghost Layers have been transferred
    - Perform computation of border edges

---
Cache Blocking
- After MPI and OpenMP hybrid implementation is working, we will analyze for what problem size does Cache Size become a bottleneck.
- We will perform Cache Blocking Optimization, to remove bottleneck issues.

---
Recommendations ?
Questions ?